## Slide 1: Home Automation with Raspberry Pi
Kevin Kuo
Advisor: Professor Wei Yu

## Slide 2: Topics of Discussion
Introduction
Platform Selection
  Wireless Protocol
  Hardware
  Software
Project Stages
Future Work/Considerations
Conclusions

## Slide 3: Introduction
About Me
Raspberry Pi
Project Objective/Goal
  Design and integrate a Raspberry Pi as a “smart home” device and determine how a small use case can be applied to larger home automated networks.

## Slide 4: Platform Selection
Wireless Protocol
  WiFi (Google Home, Amazon Alexa, other proprietary WiFi based protocols)
  ZigBee
  ZWave
Hardware
  Raspberry Pi GPIO Accessories
    5mm LED diode
    Light Sensor
  Z-Wave Transceiver (Raspberry GPIO Daughter Card vs. UZB1
  Leviton Plug-In Outlet with Z-Wave Technology

## Slide 5: Platform Selection (cont’d)
Software
  Z-Way Smart Home Controller Software
    Web User Interface
    Z-Way Essentials: Development API
  Python 2.7.13
    GPIO
    pandas
    numpy

## Slide 6: Project Stages
GPIO Breadboard and LED
  Familiarization with GPIO functions and breadboard
  Write and execute simple Python code to turn LED on and off
Light Sensor
  Set up light sensor and capacitor and then read light sensor input
  Python code for this allows user to calibrate the sensor readout for the environment
Z-Wave Setup
  No project code involved
  ZWay – Smart Home Controller
  ZWave Controller USB Dongle
  Leviton Plug-In Outlet + Outlet Tester

## Slide 7: Project Stages
Leviton Plug-In Outlet Activation/Deactivation
  Accomplish programmatically using an open URL request to Zway
Moving/Rolling Averages
  Python pandas and numpy
  Smooth out light sensor reading
Turn on/off ZWave Outlet based on light sensor reading

## Slide 8: Future Work/Considerations
ZWave sensor input and GPIO output
  ZWay API supports this
ZWave project testing over WiFi network
  Instead of just 1 Raspberry Pi serving as both GPIO
Market options and cost for smart home solutions
  ~$80 for Raspberry Pi kit
  ~$35 for ZWave outlet
  ~$30 USB dongle license
May be viable interfacing/implementing custom sensors using GPIO
Increased processing power of next Raspberry Pi 4

## Slide 9: Conclusion/Questions?